## Slide 1: The Slow Death of Heavy Equipment: How to Make it Happen Faster!
Sennebogen LLC
Constantino Lannes
President & CEO

## Slide 2
Why Maintenance ???
Lower owning and operating costs
  Extended component and machine life
  Less down time, higher availability
  Lower fuel consumption
  Higher resell value
Higher Safety
  Lower risk of accidents

## Slide 3
Maintenance Intervals
Daily checks
Preventive Maintenance
Repairs
Structural inspections
Third party inspections
What is your strategy in maintenance?
What is your strategy costing you?

## Slide 4: Are you preforming daily maintenance checks?

## Slide 5
excessive wear, damage or leaks on boom / stick cylinders and safety check valves
excessive wear, damage or leaks on outrigger cylinders
excessive wear, damage or leaks on cab elevating cylinder
excessive wear, damage or leaks on hydraulic hoses
damage or leaks on grapple cylinders
excessive wear, damage on magnet cable
damage or leaks on transmission / travel motor / axle hubs
damages on boom / stick
damages on under carriage
fluid level, leakage engine oil
fluid level, leakage engine coolant
fluid level, leakage swing gear oil
fluid level, damage hydraulic tank
fluid level, damage diesel fuel tank
Daily Inspection

## Slide 7
No Maintenance Results
Cause Dirty air filter
Result Engine replacement

## Slide 8
Cause Air filter damaged
Result Engine replacement
No Maintenance Results

## Slide 9
No Maintenance Results
Cause Engine eating dust
Result
Blowby pressure is so high its shooting dipstick out of engine

## Slide 10
No Maintenance Results
Cause Dirty cab filter
Result A/C compressor failure

## Slide 11
No Maintenance Results
Cause Missing fuel screen
Missing fuel cap
Result Exchange of all injectors & fuel pump 1-2 day down time Expensive repair costs

## Slide 12
No Maintenance Results
Cause No grease
Result New bushings, line boring, … 5-10 days machine down time Expensive repair costs

## Slide 13
No Maintenance Results
Cause Hydraulic tank dirty around return filter
Result Hydraulic oil contamination Drain tank & flush system Hydraulic component failures

## Slide 14
No Maintenance Results
Cause Loose counterweight holding bolts
Result Safety hazard

## Slide 15
No Maintenance Results
Cause Yoke not shimmed properly
Result Wear and tear on pins and Bushings & damage to Structural components

## Slide 16
No Maintenance Results
Cause Contamination hydraulic oil
Result Hydraulic component failures

## Slide 17
No Maintenance Results
Cause Damaged grapple cylinders
Result Hydraulic oil contamination Drain tank & flush system Hydraulic component failures

## Slide 18
No Maintenance Results
Cause Low oil level swing gear lubrication
Dirt in the reservoir
Result Swing gear failure

## Slide 19
No Maintenance Results
Cause Bent steps
Result Safety hazard

## Slide 20: What’s the worst that can happen?

## Slide 21
No Maintenance Results
Cause Dirt
Result Hose failures & fire

## Slide 22
No Maintenance Results
Cause Belts damaged
Result Engine overheating
Engine premature failure

## Slide 23
No Maintenance Results
Cause Leaking engine air suction line
Result Loss of engine performance Engine contamination Engine premature failures

## Slide 24
No Maintenance Results
Cause Poor repairs to wiring harness
Result Constant coil failure Low machine availability
Difficult trouble shooting Can cause equipment fire

## Slide 25
No Maintenance Results
Cause Leaking hydraulic hoses
Result Safety hazard Loosing machine performance Can cause equipment fire

## Slide 26
No Maintenance Results
Cause Leaking fuel lines
Result Safety hazard System contamination Can cause equipment fire

## Slide 27
No Maintenance Results
Cause Exhaust pipes insulation damaged
Result
Excessive heat in the engine compartment
Damage to fuel and hydraulic lines
Safety hazard Can cause equipment fire

## Slide 28
No Maintenance Results
Cause Dirt in the engine compartment
Result Safety hazard Fire

## Slide 29
No Maintenance Results
Do you want to go there???

## Slide 30
Improper maintenance increases your owning costs, decreases your uptime and creates a safety hazard to the operation and its environment.

## Slide 31: Questions???
Constantino Lannes
704-340-8232
clannes@sennebogenllc.com